## Slide 1: Inter-Integrated Circuit
Synchronous, multi-controller/multi-target (controller/target), packet switched, single-ended, serial communication bus.
Widely used for attaching lower-speed peripheral ICs to processors and microcontrollers in short-distance, intra-board communication.
https://learn.sparkfun.com/tutorials/i2c/all

## Slide 2: i2c signal
https://www.utmel.com/blog/categories/integrated%20circuit/what-is-inter-integrated-circuit-i2c

## Slide 3: Modes
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 4: Read and Write
Understanding the I2C Bus (ti.com)

## Slide 5: Logic Design
Data1 (8Bit)
Data2 (8Bit)
ACK (1Bit)
ACK (1Bit)
Slave Address (7Bit) + W
Slave Register Address (8Bit)
ACK (1Bit)
ACK (1Bit)
Mater
Slave
Data1 (8Bit)
Data2 (8Bit)
ACK (1Bit)
ACK (1Bit)
Slave Address (7Bit) + W
Slave Register Address (8Bit)
ACK (1Bit)
ACK (1Bit)
Mater
Slave
Write
Read
Slave Address (7Bit) + R
ACK (1Bit)

## Slide 6: Master Flow Chart
idle
Start write
Shift out (Send bits by shift register)
Receive acknowledge (From slave)
Stop
Master Write Process
write enable signal (From controller)

## Slide 7: Slave Flow Chart
idle
Shift (Receive)
Send acknowledge
Write (Register File)
Write Slave Process
sda_falling
idle

## Slide 8: Master Flow Chart
idle
Start read
Shift out (Send slave address, R/W signal and slave register address)
Receive acknowledge (From slave)
Stop
Master Read Process
Shift in (Receive data from slave)
Send acknowledge
read enable signal (From controller)

## Slide 9: Slave Flow Chart
idle
Shift (Receive)
Send acknowledge
Read Slave Process
sda_falling
Send
Receive acknowledge
idle

## Slide 10
MASTER
clk
reset
clk_div
open_drain (always 1)
chip_addr [7]
reg_addr [8]
write_en
read_en
write_mode
status [4]
done
busy
data_in [16]
data_out [16]
sda_in
sda_out
sda_oen
scl_in
scl_out
scl_oen
SDA
SCL
INPUT
OUTPUT
Interal registers
sr [32] (Shift register) writing
sr_count [6] reading
byte_count [3] in_prog
scl_count [2]
clk_count [12]
sda_s
sda_reg
oen_reg
scl_s

## Slide 11
SLAVE
clk
reset
open_drain (always 1)
chip_addr [7]
done
busy
data_in [16]
data_out [16]
sda_in
sda_out
sda_oen
scl_in
scl_out (0)
scl_oen (1)
SDA
SCL
INPUT
OUTPUT
Interal registers
sr [8] (Shift register) rw_bit
sr_send [16] nack
reg_bytes [2] writing
addr_bytes[2] reading
scl_count [2] continuing
clk_count [12]
chip_addr_reg [7]
sda_s
sda_reg
oen_reg
scl_s
scl_ss
sda_ss
reg_addr [8]

## Slide 12: Open Drain
SDA is high when idle.

## Slide 13: Open-Drain Pulling Low and Releasing
Understanding the I2C Bus (ti.com)

## Slide 14
Chip
I2C
Master
Slave
SDA
SCL
Control Logic
Data Path
Register File [16bit * 256]
Data Register [16]
Register for slave address + W/R [8]
Slave Register address [8]
Write enable [1]
Read enable [1]
sda_in
sda_out_en
sda_out (Ground)
scl_in
sda_out_en
sda_ out (Ground)
sda_in
sda_out_en
sda_out (Groud)
scl_in
scl_out_en
scl_out (Ground)
VDD
Pull-up R
Pull-up R
Open drain design

## Slide 15: i2c_write_tb

## Slide 16: i2c_write_tb

## Slide 17: i2c_write_tb Master

## Slide 18: i2c_write_tb Slave

## Slide 19: i2c_read_tb

## Slide 20: i2c_read_tb

## Slide 21
I2C
Input clk
Input reset
Input clk_div
Input open_drain
Input chip_addr
Input reg_addr
Input data_in
Input write_en
Input write_mode
Input read_en
Output status
Output done
Output busy
Output data_out
Input sda_in
Input scl_in
Output sda_out
Output sda_oen
Output scl_out
Output scl_oen
Master
Input clk
Input reset
Input open_drain
Input chip_addr
Output reg_addr
Input data_in
Output write_en
Output data_out
Output done
Output busy
Input sda_in
Input scl_in
Output sda_out
Output sda_oen
Output scl_out
Output scl_oen
Slave
Input clk
Input reset
Input clk_div
Input open_drain
Input chip_addr
Input reg_addr
Input write_en
Input write_mode
Input read_en
Output status
Input chip_id
Output slave_reg_addr
Output slave_write_en
Master Logic
Slave Logic
Data Path
Input data_in
Output data_out
Output done
Output busy
MUX
MUX
MUX
MUX
MUX
MUX
Output sda_out
Output sda_oen
Output scl_out
Output scl_oen
MUX
Input sda_in
Input scl_in
SDA and SCL
MUX
enable
enable? Master, Slave